LABORATORY REPORT NO. AE1100112/DL01713 A/07

| WATER ANALYSIS REPORT |
| --- |
| SAMPLING CONDITIONS: |  |  |
| Sample No. | : | DL 01713 A |
| Sample Identification | : | “A” |
| Sampling Date & Time | : | - |
| Sampling Point | : | - |
| Specific gravity at 60/60 ºF | : | 1.0108 |
| pH at 25 °C | : | 7.5 |
| Conductivity ((s/cm) @ 75 ºF | : | 22100 |
| Resistivity @ 75 ºF (ohm-m) | : | 0.4525 |
| Total Dissolved Solids (mg/L) | : | 13595 |
| Alkalinity (as MgCaCO3/L) | : | - |
| Dissolved H2S (mg/L) | : | - |
| Cations | Mg/l | Meq/l |
| Sodium | 3946 | 171.56 |
| Calcium | 610 | 30.50 |
| Magnesium | 277 | 22.80 |
| Iron | 0.2 | 0.01 |
| Barium | ND | ND |
| Potassium | 107 | 2.74 |
| Strontium | 31 | 0.71 |
| Anions | Mg/l | Meq/l |
| Chloride | 7007 | 197.66 |
| Bicarbonate | 46 | 0.75 |
| Sulphate | 1401 | 29.19 |
| Carbonate | Zero | Zero |
| Hydroxide | Zero | Zero |

Ravi P

Laboratory Manager

LABORATORY REPORT NO. AE1100112/DL01713 B/07

| WATER ANALYSIS REPORT |
| --- |
| SAMPLING CONDITIONS: |  |  |
| Sample No. | : | DL 01713 B |
| Sample Identification | : | “B” |
| Sampling Date & Time | : | - |
| Sampling Point | : | - |
| Specific gravity at 60/60 ºF | : | 1.0112 |
| pH at 25 °C | : | 8.0 |
| Conductivity ((s/cm) @ 75 ºF | : | 22400 |
| Resistivity @ 75 ºF (ohm-m) | : | 0.4464 |
| Total Dissolved Solids (mg/L) | : | 14564 |
| Alkalinity (as MgCaCO3/L) | : | - |
| Dissolved H2S (mg/L) | : | - |
| Cations | Mg/l | Meq/l |
| Sodium | 4110 | 178.71 |
| Calcium | 762 | 38.10 |
| Magnesium | 281 | 23.13 |
| Iron | <0.1 | <0.01 |
| Barium | ND | ND |
| Potassium | 106 | 2.72 |
| Strontium | 30 | 0.68 |
| Anions | Mg/l | Meq/l |
| Chloride | 7298 | 205.87 |
| Bicarbonate | 76 | 1.25 |
| Sulphate | 1706 | 35.54 |
| Carbonate | Zero | Zero |
| Hydroxide | Zero | Zero |

Ravi P

Laboratory Manager